Commissioning Sequence Progress Check Sheet

System: LSI Heating Hot Water Systems

Overview: Three heat exchangers (HX-1, 2, and 3) convert steam to 180ºF hot water for the perimeter heating hot water systems and the reheat hot water systems. There are two perimeter systems and two reheat systems. One air separator and one expansion tank connected to the heat exchanger outlets serve the entire system. The heat exchangers operate in sequence with the first HX being primary and the second and third HX as secondary. Each heat exchanger is a U-tube type with 15,000 mbh capacity and 1500 gpm flow.

Office/Lab Reheat System: HWHP-1 and 2 supply HHW to AHUs-1, 2, 7, 8, lab/office reheat coils and finned tube. The system supplies the same constant temperature water (180ºF) that is produced by the heat exchangers. There are no controls that maintain this temperature specifically for the reheat system. One pump is a stand-by pump. The pumps are controlled by VSDs. The pumps are horz. split case type with 3000 gpm capacity.

Vivarium Reheat System: HWHP-3 and 4 supply HHW to AHUs-3, 4, 5, 6, and Vivarium reheat coils. The system supplies a constant temperature water (150ºF) that is produced by a three way mixing valve tapping off of the heat exchanger loop. One pump is a stand-by pump. The pumps are controlled by VSDs. The pumps are horz. split case type with 725 gpm capacity.

North Perimeter System: HWHP-5 and 6 supply HHW to finned tube and unit heaters on the north half of the building. The system supplies heating water that is produced by a three way mixing valve tapping off of the heat exchanger loop. The water is reset between 140 and 180ºF based on the U of M global OA sensor. One pump is a stand-by pump. The pumps provide constant flow (no VSDs). The pumps are end suction base mounted type with 110 gpm capacity.

South Perimeter System: HWHP-7 and 8 supply HHW to finned tube and unit heaters on the south half of the building. The system supplies heating water that is produced by a three way mixing valve tapping off of the heat exchanger loop. The water is reset between 140 and 180ºF based on a solar sensor. One pump is a stand-by pump. The pumps provide constant flow (no VSDs). The pumps are end suction base mounted type with 50 gpm capacity.

Commissioning Sequence Progress Check Sheet

System: Heat Exchanger System

Cx Sequence:

Initial acknowledgment and date when item is complete.

Acknowledgements

Owner		Contractor

Shop Drawings Approved

_____			Heat Exchanger

_____	Major Components Delivered (Heat Exchangers, Air Separator, Expansion Tank)

_____		Pre-Installation Checklist Completed (HX)

_____          _____       	Installation Instructions Provided (HX)

_____		Installations Complete

_____		Controls Complete (subcontractor)

_____		Controls Complete (UM DDC)

_____         _____     	Flushing/Cleaning Plan Submitted/Approved

_____		_____		Flushing Complete

_____		_____		Pre-start Check Sheet Complete

_____	     	 _____		Start – up Notification Submitted

_____		_____		Functional Testing Check Sheet Complete

_____         _____      	Training Scheduled

_____         _____      	Training Completed

_____      	All Punch-list Items Completed

_____ 		_____		Contract Commissioning Requirements Completed

Commissioning Sequence Progress Check Sheet

System: Office/Lab HHW Reheat Systems

Cx Sequence:

Initial acknowledgment and date when item is complete.

Acknowledgements

Owner		Contractor

_____		Shop Drawings Approved: VSDs, Pumps HWHP-1, 2

_____		Major Components Delivered: Pumps, VSDs

_____		Pre-Installation Checklist Completed (Pumps, VSDs)

_____          _____       	Installation Instructions Provided (Pumps, VSDs)

_____		_____ 		Pipe / Pump alignment confirmed

UM Cx to view before bolting pipe to pump flanges.

_____		Mechanical Installation Complete

_____		Electrical Installation Complete

_____		Controls Complete (subcontractor)

_____		Controls Complete (UM DDC)

_____         _____     	Flushing/Cleaning Plan Submitted/Approved

_____		_____		Flushing Complete

_____		Pre-start Check Sheet Complete, Pumps

_____		Pre-start Check Sheet Complete, VSDs

_____	     	 _____		Start – up Notification Submitted

_____		_____		Functional Testing Check Sheet Complete

_____         _____      	Training Scheduled

_____         _____      	Training Completed

_____      	All Punch-list Items Completed

_____ 		_____		Contract Commissioning Requirements Completed

Commissioning Sequence Progress Check Sheet

System: Vivarium HHW Reheat System

Cx Sequence:

Initial acknowledgment and date when item is complete.

Acknowledgements

Owner		Contractor

_____		Shop Drawings Approved: VSDs, Pumps HWHP-3, 4

_____		Major Components Delivered: Pumps, VSDs

_____		Pre-Installation Checklist Completed (Pumps, VSDs)

_____          _____       	Installation Instructions Provided (Pumps, VSDs)

_____		_____ 		Pipe / Pump alignment confirmed

UM Cx to view before bolting pipe to pump flanges.

_____		Mechanical Installation Complete

_____		Electrical Installation Complete

_____		Controls Complete (subcontractor)

_____		Controls Complete (UM DDC)

_____         _____     	Flushing/Cleaning Plan Submitted/Approved

_____		_____		Flushing Complete

_____		Pre-start Check Sheet Complete, Pumps

_____		Pre-start Check Sheet Complete, VSDs

_____	     	 _____		Start – up Notification Submitted

_____		_____		Functional Testing Check Sheet Complete

_____         _____      	Training Scheduled

_____         _____      	Training Completed

_____      	All Punch-list Items Completed

_____ 		_____		Contract Commissioning Requirements Completed

Commissioning Sequence Progress Check Sheet

System: North Perimeter HHW System

Cx Sequence:

Initial acknowledgment and date when item is complete.

Acknowledgements

Owner		Contractor

_____		Shop Drawings Approved: Pumps HWHP-5, 6

_____		Major Components Delivered: Pumps

_____		Pre-Installation Checklist Completed (Pumps)

_____          _____       	Installation Instructions Provided (Pumps)

_____		_____ 		Pipe / Pump alignment confirmed

UM Cx to view before bolting pipe to pump flanges.

_____		Mechanical Installation Complete

_____		Electrical Installation Complete

_____		Controls Complete (subcontractor)

_____		Controls Complete (UM DDC)

_____         _____     	Flushing/Cleaning Plan Submitted/Approved

_____		_____		Flushing Complete

_____		Pre-start Check Sheet Complete, Pumps

_____	     	 _____		Start – up Notification Submitted

_____		_____		Functional Testing Check Sheet Complete

_____         _____      	Training Scheduled

_____         _____      	Training Completed

_____      	All Punch-list Items Completed

_____ 		_____		Contract Commissioning Requirements Completed

Commissioning Sequence Progress Check Sheet

System: South Perimeter HHW System

Cx Sequence:

Initial acknowledgment and date when item is complete.

Acknowledgements

Owner		Contractor

_____		Shop Drawings Approved: Pumps HWHP-7, 8

_____		Major Components Delivered: Pumps

_____		Pre-Installation Checklist Completed (Pumps)

_____          _____       	Installation Instructions Provided (Pumps)

_____		_____ 		Pipe / Pump alignment confirmed

UM Cx to view before bolting pipe to pump flanges.

_____		Mechanical Installation Complete

_____		Electrical Installation Complete

_____		Controls Complete (subcontractor)

_____		Controls Complete (UM DDC)

_____         _____     	Flushing/Cleaning Plan Submitted/Approved

_____		_____		Flushing Complete

_____		Pre-start Check Sheet Complete, Pumps

_____	     	 _____		Start – up Notification Submitted

_____		_____		Functional Testing Check Sheet Complete

_____         _____      	Training Scheduled

_____         _____      	Training Completed

_____      	All Punch-list Items Completed

_____ 		_____		Contract Commissioning Requirements Completed