Commissioning Sequence Progress Check Sheet

System: Energy Recovery System

Overview: AHU-1, 2, 3, 4, 5, and 6 each have an energy recovery coil. Floors 1, 3, 4, 5, and 6  have a Strobic fan exhaust system dedicated each floor. There is one energy recovery coil in each Strobic fan exhaust system. This makes 5 exhaust energy recovery coils and 6 supply energy recovery coils. The coils are connected through common piping and a 40% glycol solution is circulated by pumps P-1 and P-2. These pumps have a primary/stand-by arrangement. The flow is 1780 gpm. Controls prevent the exhaust fluid temperature from falling below 35ºF and work in sequence with the AHU controls to maintain supply air temperature. Refer to M9-1.04 for controls. A glycol feeder keeps the system charged with glycol solution

Cx Sequence:

Acknowledgements

Owner		Contractor

_____		Shop Drawings Approved: (Pumps)

_____		Major Components Delivered: (Pumps, Piping, Coils, Feeder)

_____		Pre-Installation Checklist Completed (Pumps)

_____          _____       	Installation Instructions Provided (Pumps, Glycol Feeder)

_____		Controls Complete (subcontractor)

_____		Controls Complete (UM DDC)

_____		_____ 		Pipe / Pump alignment confirmed

UM Cx to view before bolting pipe to pump flanges.

_____		Pressure Testing Complete

_____         _____     	Flushing/Cleaning Plan Submitted/Approved

_____		_____		Flushing Complete

_____		_____		Pre-start Check Sheet Complete

_____	     	 _____		Start – up Notification Submitted

_____		_____		Functional Testing Check Sheet Complete

_____         _____      	Training Scheduled

_____         _____      	Training Completed

_____      	All Punch-list Items Completed

_____ 		_____		Contract Commissioning Requirements Completed