Editors Note: Blue text not to be changed.  Remember to fill in system name in title and footer.

PRE-START CHECKLIST- PANELBOARD - EMERGENCY POWER

University of Michigan Plant Extension

Commissioning & Plan Review Department

Phone (734) 615-7168  Fax (734) 936-3334

This document shall be filled out by the contractor and provided to the UM Commissioning Engineer at least 7 days in advance of the actual equipment start-up. Note “NA” for not applicable or “NO” for problem or non-compliance. This document is to be used in conjunction with the manufacturer’s pre-start checklist.

Project Name: XXX			 		Project Number: XXXX-XX-XXX

Tag No.			Model No.			Serial No.

Check     Item							Comments

General:

___ Panel nameplate data is complete and legible ______________________________________________

___ Voltage rating (record): ___________________________________________________________

___ Ampere rating (record): ___________________________________________________________

___ MLO or Main Breaker (record): _____________________________________________________

___ Phase and wire (record): ___________________________________________________________

___ AIC rating (record): ______________________________________________________________

___ Panel complies with approved shop drawings ______________________________________________

___ All connections are torqued to manufacturer recommendation _________________________________

___ Test report reviewed and approved ______________________________________________________

___ Proper clearance is obtained ____________________________________________________________

___ 3'-6" minimum in front and 6'-6" AFF minimum _________________________________________

___ Typed panelborad schedule is complete and accurate ________________________________________

___ Equipment is clean, protected from dust, and securable _______________________________________

Breakers:

___ Complies with panelboard schedule ______________________________________________________

Branch Circuits:

___ Phasing is correctly identified ___________________________________________________________

Start-Up:

___ Start-up scheduled for: ____________________, to be conducted by: __________________________

___ Start-up notification faxed to UM commissioner 7 days in advance of scheduled start-up.

Remarks:____________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

## Completed by (print): ___________________________Company: _________________________

Signed: ____________________________________________Date:________________________________