FUNCTIONAL TEST – PLUMBING FIXTURES

University of Michigan Plant Extension

Commissioning and Plan Review Department

Phone (734) 615-7168 Fax (734) 936-3334

This is not a punch list.  The engineer of record, not the commissioning team, performs Punch listing.

Project Name: XXX					Project Number: XXXX-XX-XXX

Tag No.			Model No.			Serial No.

Attendees:

1) _________________________________________ 2)____________________________________

3) _________________________________________ 4)____________________________________

5) _________________________________________ 6)____________________________________

7) _________________________________________ 8)____________________________________

Is system operating or is this initial start-up? _________________________________________________

Is the Pre-Start Checklist Complete? _______________________________________________________

Check     Item	Comments

Water Closets, Urinals, Faucets:

___ Check piping and isolation valves for leaks. Open and close valves to check for proper operation

___ Check Flush valves/ Faucets for operation.

___ Water pressure adequate.

Fountains:

___ Check piping and isolation valves for leaks. Open and close valves to check for proper operation

___ Bubbler adjusted

___ Free draining

___ Compressor Operation (cools water, quiet operation, etc.)

___ Electronic sensor adjusted (Hands off unit only)

___ Time delay to prevent activation by passers-by is adjusted (Hands off unit only)

___ Maximum on feature operates at 30 – 35 seconds (Hands off unit only)

Emergency Fixtures:

___ Water pressure adequate.

Air, gas, vacuum lab valves:

___ pressure/flow adequate

System Start-Up:

___ Start-up scheduled for: ____________________, to be conducted by: __________________________

___ Start-up notification faxed to UM commissioner 7 days in advance of scheduled start-up.

Remarks:

## Completed by (print): _______________________Company: __________________________

Signed: _______________________________________ Date: _________________________________

Remarks: