FUNCTIONAL TEST -RETURN FANS

University of Michigan Plant Extension

Commissioning & Plan Review Department

Phone (734) 615-7168 Fax (734) 936-3334

This is not a punch list.  The engineer of record, not the commissioning team, performs the Punch list.

Project Name: XXX					Project Number: XXXX-XX-XXX

Tag No.			Model No.			Serial No.

Start-up Date: _________________________

Attendees:

1) _________________________________________ 2)____________________________________

3) _________________________________________ 4)____________________________________

5) _________________________________________ 6)____________________________________

Check     Item							Comments

# General

Is system operating or is this initial start-up? _________________________________________________

Is the Pre-Start Checklist Complete? _______________________________________________________

# Fan

_______  Is there any drag when fan is hand rotated? __________________________________________

_______  Does the fan have the correct rotation? ______________________________________________

_______  Is the drive belt tension correct? ___________________________________________________

_______  Is there any unusual vibration? (Check throughout fan range if variable speed)______________

_______  Is there any unusual noise? _______________________________________________________

_______  Do the backdaft damper open and close smoothly?  ____________________________________

_______  Do the control dampers function?  _________________________________________________

Measured amp draw (A/B/C):  ______ / _______ / ________

Measured voltage: (AB/BC/AC): ______ / _______ / _______

Controls

______HOA switches and lights work: _____________________________________________________

______Alarms activate locally: ____________________________________________________________

______Alarms activate via DDC: __________________________________________________________

______Fans will start/stop/change speed via DDC_____________________________________________

______Current Sensor operates via DDC_____________________________________________________

Remarks:

## Completed by (print): __________________________ Company: ______________________________

Signed: _______________________________________ Date: _________________________________