Commissioning Sequence Progress Check Sheet

System: Stair Pressurization Systems

Overview: SF-11 and 12 are 13,500 cfm tubular centrifugal fans located in the penthouse. Each fan has a back draft damper located at the inlet and supplies air to the stairs. SF-11 serves the west stairs. SF-12 serves the east stairs. The fire alarm system will start the fans and open a relief air damper at the top of the stairs. A static pressure sensor in the stairs modulates the airflow through a VSD at each fan to maintain a pressure setting of 0.15 inches WG.  A smoke purge mode can be manually started/stopped at the fire alarm panel. In this mode the fans operate at full speed to maximum the airflow.

Cx Sequence:

Initial acknowledgment and date when item is complete.

Acknowledgements

Owner		Contractor

_____		Shop Drawings Approved

Fans, Ductwork, Dampers

_____       	Major Components Delivered

_____          	_____       	Installation Manuals submitted

_____       	Pre-Installation Check Sheets Completed (SF-11, SF-12)

_____	     	Mechanical Complete

_____       	Electrical Complete

_____ Fan    _____ Fire Control Panel

_____      	Controls Complete (subcontractor)

_____      	Controls Complete (UM DDC)

_____          	_____      	Pre-Start Check sheet Completed

_____		   	_____		Start – up Notification Submitted

_____          	_____      	Functional Testing Check Sheet Completed

_____          	_____       	Training Scheduled

_____          	_____       	Training Completed

_____      	All Punch-List Items Completed

_____		    	_____		Contract Commissioning Requirements Completed