Commissioning Sequence Progress Check Sheet

System: LSI Steam and Condensate System

Overview: A 14 inch LPS (9#), an 8 inch MPS (60#), and a 4 inch LPC enter the northeast corner of the building from the utility tunnel.

The MPS serves the clean steam generator (SG-1) and all lab equipment (Bulk Sterilizer, Medium Steam Sterilizer, Cage and Rack Washer, Tunnel Cage Washer, Small Sterilizers, and Glassware Washers).

The LPS serves the humidifiers for AHU-1, AHU-2, AHU-3, AHU-4, AHU-5, AHU-6 and the heat exchangers for heating hot water (HX-1) and domestic water (HX-2).

Steam Generator SG-1 creates clean steam (9#) that is used by the office humidifiers for AHU-7 and AHU-8.

Condensate from the MPS system collects to five different flash tanks where the pressure is reduced. The condensate on the first floor passes through two of these flash tanks, two separate condensate coolers, and then to condensate pumps CP-1 and CP-2 before discharging to the low pressure condensate system. The condensate above the first floor passes through three different flash tanks and discharges directly to the LPC system. Condensate from the LPS system also discharges to he LPC (9#) system. This LPC system then drains out a 4 inch line to the utility tunnel.

Condensate from the clean steam system passes through a condensate cooler and discharges to a floor drain.

There are a total of 4 condensate coolers, 5 flash tanks, and 2 condensate pumps shown on the drawings.

Cx Sequence:

Acknowledgements

Owner		Contractor

Shop Drawings Approved

_____			Flash Tanks, Condensate Coolers, Condensate Pumps

_____ 			Steam Meters

_____		Welder Certifications submitted

_____		Major Components Delivered

_____		Pre-Installation Checklist Completed

_____       	Installation Instructions Provided

_____		Installation Complete

_____ 		Pressure Testing Complete

_____           	_____ 		Flushing/Cleaning Plan Submitted/Approved

_____		      _____		Flushing Complete

_____		Pre-test checks complete

_____		   	_____		Start – up Notification Submitted

_____		   	_____		Functional Test Check Sheet Completed

_____            	_____      	Training Scheduled

_____            	_____      	Training Completed

_____      	All Punch-list Items Completed

_____ 			_____		Contract Commissioning Requirements Completed